Chroma-Matic

“Everthing You Always Wanted to Know but Were Afraid to Ask”

Last updated 14 Nov '06  A.S.

Port Mapping for RCM3200

Port	I/O	Function

====	===	=================================================

PB0	 O	Serial Clock

PB2	 O	Serial Data out

PB3	  I	ADC Data in

PB4	 O	ADC /CS

PB5	 O	DAC LD

PB6	 O	Charge Pump/DAC switch (0 = DAC, 1 = CP)

PB7	 O	Charge Pump Linear/Integrate mode (0 = integrate, 1 = linear)

PC0	 O	LED 1, laser locked

PC1	  I	Front Switch 1 (LSB)

PC2	 O	LED 2 (reserved for future use)

PC3	  I	Front Switch 2

PC4	 O	LED 3 (reserved for future use)

PC5	  I	Front Switch 3 (MSB)

PD4	  O	Prescaler N1 (n2=0, n1=0 is ÷ 8;  0,1 is ÷ 16;  1,0 is ÷ 32;  1,1 is ÷ 64)

PD5	  O	Prescaler N2

PE1	 O	DDS FUD

PE3	 O	DDS P0

PE4	 O	DDS P1

PE5	  I	BNC, Adwin trigger (inverted)

PE6	 O	DDS RST

PE7	 O	BNC, 'scope trigger

PF0-7	 I/O	DDS data bus

PG0-5	 O	DDS address bus

PG6	 O	DDS /WR

PG7	 O	DDS /RD

ADC Channels

Chan.	Description

====	=================================================

0	Charge pump output

1	Charge pump reference current

2	User control (if connected)

3	ROSA signal strength

Front Switch Settings

Position	Description

======	=================================================

0	Pushbutton, push to execute setting

1	DAC sweep, for laser setup

2	Reset

3-7	Stored Configurations 0-4