Two Photon Source      5 July 2006  A.S.

Port Mapping for RCM3200

Port	I/O	Function

====	===	=================================================

PA0-7		Reserved for ethernet

PB0	 O	/ECL_CURRENT_CS, DAC, 12-bit, 0 to 140mA

PB2	 O	/ECL_TEC_EN, low enables TEC

PB3	 O	/ECL_PIEZO_CS, DAC, 12-bit, +63.3 to 0V

PB4	 O	/ECL_NARROW_MODE, high enables the active cavity correction to reduce noise

PB5	 O	/INJ_CURRENT_CS, DAC, 12-bit, 0 to 140mA

PB6	 O	/INJ_TEC_EN, low enables TEC

PB7	 O	SCAN_EN, high adds a 1mA load to all piezo supplies to increase -dV/dt for scanning

PC0	 O	/SCAN_X_CS, DAC, 12-bit, X-axis output to 'scope, for scanning

PC1	 I	SW1, front panel switch, bit 0

PC2	 O	/SCAN_Y_CS, DAC, 12-bit, Y-axis output to 'scope, for scanning

PC3	 I	SW1, front panel switch, bit 1

PC4	 O	SCLK, serial clock for all DACS

PC5	 I	SW1, front panel switch, bit 2

PC6-7	 	Reserved for programming port, J3

PD0		Reserved for ethernet

PD2-3		Reserved for ethernet

PD4-5		Reserved for ethernet, maybe, so do not use

PD6-7		Reserved for ethernet

PE0	 	Reserved for ethernet

PE1	 O	/CONV, ADC, start conversion

PE2		Reserved (for ?)

PE3	 I	BUSY, ADC, high during a conversion

PE4	 O	/RD, ADC read enable

PE5	 O	/WR, ADC write enable

PE6	 O	/CS, ADC chip select

PE7	 I	SW1, front panel switch, bit 3

PF0-7	I/O	Data bus, bits 0-7

PG0-3	I/O	Data bus, bits 8-11

PG4	 O	SDATA, serial data for all DACs

PG5	 O	/DN_HTR_EN, low enables the heater on the down conversion crystal

PG6	 O	/CS_DOWN, DAC, 12-bit, +63.3 to 0V

PG7	 O	/CS_UP, DAC, 12-bit, +63.3 to 0V

ADC Channels    All are 12-bit

ADC	Description

===	=================================

0	ECL photodiode

1	ECL TEC current (0 to 7.35A, limited to about 1.5A)

2	ECL temperature (+29.5° to +1.6°)

3	Injection laser TEC current (0 to 7.35A, limited to about 1.5A)

4	Injection laser temperature (+29.5° to +1.6°)

5	Up converter photodiode

6	Down converter photodiode

7	Front panel 10-turn pot

DAC Channels    All are 12-bit

DAC	Description

===	=================================

0	ECL laser current (0 to +80mA)

1	ECL piezo voltage (+63.3 to 0V)

2	Injection laser current (0 to +80mA)

3	Up converter piezo voltage (+63.3 to 0V)

4	Down converter piezo voltage (+63.3 to 0V)

5	X-axis (0 to +4.095V)

6	Y-axis (0 to +4.095V)

Status Byte   32 bytes, once a second

Byte	Description

===	=================================

0-15	ADC channels 0-7, two bytes per channels (4 MSB of MS byte are zeros)

16	unused

17	Status byte as follows (logic “1” indicates on):

17.0		ECL TEC status

17.1		Injection laser TEC status

17.2		Scan loads enabled status

17.3		Down converter heater status

17.4		ECL line narrowing status

17.5-7		unused, currently all zeros

18-19	ECL current DAC setting (for all DACs, 4 MSB of MS byte are zeros)

20-21	ECL piezo DAC setting

22-23	Injection laser current DAC setting

24-25	Up converter piezo DAC setting

26-27	Down converter piezo DAC setting

28-29	X-axis output DAC setting

30-31	Y-axis output DAC setting

Back Panel Connectors

Pin	ECL			Injection Laser	Up/Down Cavities

===	=============	=============	=============

1	Laser Anode*		Laser Anode*		Up Piezo+

2	Laser Cathode*	Laser Cathode*	Up Piezo-

3	TEC +			TEC+			Down Piezo+

4	TEC -			TEC-			Down Piezo-

5	Thermister		Thermister		Down thermister

6	Thermister		Thermister		Down thermister

7	Piezo+						Down heater

8	Piezo-						Down heater

9

* Add 22uF tantalum capacitor anode to cathode.