## Slide 1: Wave plates
When a beam propagates through a birefringent medium, one polarization sees more phase delay than the other.
This changes the relative phase of the x and y fields, and hence changing the polarization.
Polarization state:
Output:
}
}
Wave plate
+45° Polarization
Optic axis
-45° Polarization
x
y
z
Input:

## Slide 2: Wave plates (continued)
Wave plate output polarization state:
A quarter-wave plate creates circular polarization, and a half-wave plate rotates linear polarization by 90.
We can add an additional 2m without changing the polarization, so the polarization cycles through this evolution as d increases further.
Quarter-wave plate
Half-wave plate
(45-degree input polarization)

## Slide 3: Half-wave plate
If the incident polarization is +45° to the principal axes, then the output polarization is rotated by 90° to -45°.
When a beam propagates through a half-wave plate, one polarization experiences half of a wavelength more phase delay than the other.

## Slide 4: Wave plates and input polarization
Remember that our wave plate analysis assumes 45° input polarization relative to its principal axes. This means that either the input polarization is oriented at 45°, or the wave plate is.
Wave plate w/ axes at 0° or 90°
±45° Polarizer
Wave plate w/ axes at ±45°
0° or 90° Polarizer
If a HWP, this yields 45° polarization.
If a QWP, this yields circular polarization.
±
If a HWP, this yields 90° or 0° polarization.
If a QWP, this yields circular polarization.

## Slide 5: How not to use a wave plate
If the input polarization is parallel to the wave plate principal axes, no polarization rotation occurs!
Wave plate w/ axes at 0° or 90°
Wave plate w/ axes at ±45°
0° or 90° Polarizer
±45° Polarizer
This arrangement can, however, be useful. In high-power lasers, we desire to keep the laser from lasing and then abruptly allow it to do so. In this case, we switch between this and the previous case.

## Slide 6: Thickness of wave plates
When a wave plate has less than 2 relative phase delay, we say it’s a zero-order wave plate. Unfortunately, they tend to be very thin.
Solve for d to find the thickness of a zero-order quarter-wave plate:
Using green light at 500 nm and quartz, whose refractive indices are ne – no = 1.5534 – 1.5443 = 0.0091, we find:
This is so thin that it is very fragile and very difficult to manufacture.
d
d = 13.7 m

## Slide 7: Multi-order wave plates
A multi-order wave plate has more than 2 relative phase delay.
We can design a twentieth-order quarter-wave plate with 20¼ waves of relative phase delay, instead of just ¼:
This is thicker, but it’s now 41 times more wavelength dependent!
It’s also temperature dependent due to n’s dependence on temperature.
d
d = 561 m

## Slide 8: A thick zero-order wave plate
The first plate is cut with fast and slow axes opposite to those of the second one.
The Jones vector becomes:
First plate
Second plate
Now, as long as d1 – d2 is equal to the thin zero-order wave plate, this optic behaves like the prohibitively thin one! This is ideal.
Input
beam
Optic axes
x
y
z
Output
beam
d1
d2

## Slide 9: The Babinet Compensator rotates polarization by an arbitrary amount.
Top wedge is cut with fast and slow axes opposite to those of bottom wedge.
Slide one wedge with
respect to the other,
changing d1 and/or d2.
In practice, the two wedges are contacted.
Top wedge
Bottom wedge
Input
beam
d2
Optic axes
x
y
z
Output
beam
d1
d1