## Slide 1: Optical Activity & Jones Matrices
Ways to actively control polarization
Pockels' Effect
Kerr Effect
Photoelasticity
Optical Activity
Faraday Effect
Jones Matrices
Unpolarized light, Stokes Parameters, & Mueller Matrices

## Slide 2: The Pockels' Effect
An electric field can induce birefringence.
The Pockels' effect allows control over the polarization rotation.

## Slide 3: The Pockels Effect: Electro-optic constants

## Slide 4: The Q-Switch
In high-power lasers, we desire to prevent the laser from lasing until we’ve finished dumping all the energy into the laser medium. Then we let it lase. A Pockels’ cell is the way we do this.
The Pockels’ cell switches (in a few nanoseconds) from a quarter-wave plate to nothing.
Before switching
After switching
Pockels’ cell as wave plate w/ axes at ±45°
0° Polarizer
Mirror
Pockels’ cell as an isotropic medium
0° Polarizer
Mirror
Light becomes circular on the first pass and then horizontal on the next and is then rejected by the polarizer.
Light is unaffected by the Pockels’ cell and hence is passed by the polarizer.

## Slide 5: Q-switching
Q-switching involves:
1. Preventing the laser from lasing until the flash lamp is finished flashing, and
2. Abruptly allowing the laser to lase.
100%
0%
Time
Cavity Loss
Cavity Gain
Output intensity
This yields a short “giant” high-power pulse.
The pulse length is limited by the round-trip time of the laser and yields pulses 10 - 100 ns long.

## Slide 6: The Kerr effect: the polarization rotation is proportional to the Kerr constant and E2
where:
n is the induced birefringence,
E is the electric field strength,
K is the “Kerr constant” of the material.
Use the Kerr effect in isotropic media, where the Pockels' effect is zero.
The "AC Kerr Effect" creates birefringence using intense fields of a light
wave. Usually very high irradiances from ultrashort laser pulses are
required to create quarter-wave rotations.

## Slide 7: Photoelasticity: “Stress-induced Birefringence”
Clear plastic triangle between parallel and crossed polarizers
Parallel
Crossed
You should see this in color!

## Slide 8: Stress-Induced Birefringence in Diamond
An artificially grown diamond with nitrogen impurities
Caused by strain associated with growth boundaries
Notes: The diamond is grown as [1,1,1]sectors(right, lower left, upper left) from a tiny seed (in the centre). At the sector interfaces there is a slight crystal-lattice misalignment, which allows for the incorporation of nitrogen (slightly absorbing, see intensity image). The misalignment together with the presence of nitrogen causes a build-up of strain. The strain from one boundary dominates half of each sector (j -image).
Images from http://www.metripol.com/applications/diamonds.html

## Slide 9: More Photoelasticity
If there's not enough stress in a medium to begin with, you can always add more yourself!
Clear plastic between crossed polarizers
You can use this effect to improve the performance of polarizers.

## Slide 10: Optical Activity (also called “Chirality”)
Unlike birefringence, optical activity maintains a linear polarization throughout. The polarization rotation angle is proportional to the distance. Optical activity was discovered in 1811 by Arago.
Some substances rotate the polarization clockwise (“dextrorotatory”) and some produce a counterclockwise rotation (“levorotatory”).

## Slide 11: Right vs. left-handed materials
Most naturally occurring materials do not exhibit chirality. But those that do can be left- or right-handed.
These forms of quartz, have the same chemical formulas and structures, but are mirror images of each other. One form of quartz rotates the polarization clockwise and the other rotates it counterclockwise.

## Slide 12: Left-handed vs. right-handed molecules
The key molecules of life are almost all left-handed. Sugar is one of the most chiral substances known.
Occasionally, a molecule of the wrong chirality can cause serious illness (e.g., thalidimide) while its other “enantiomer” is harmless.
If you’d like to look for signs of life on other planets, look for chirality.

## Slide 13: Principal Axes for Optical Activity
As for birefringent media, the principal axes of an optically active medium are the medium's symmetry axes.
We consider the component of light along each principal axis independently in the medium and recombine them afterward.
In media with optical activity, the principal axes correspond to circular polarizations.

## Slide 14: Complex Principal Axes
Usually, we write the E-field in terms of its x- and y-components.
But we can equally well write it in terms of its right and left
circular components.
When the principal axes of a medium are circular, as they are
when optical activity is present, this is required. We must then
decompose linear polarization into its circular components:

## Slide 15: The Faraday Effect
A magnetic field can induce optical activity.
The Faraday effect allows control over the polarization rotation.

## Slide 16: The Faraday effect: the polarization rotation is proportional to the Verdet constant.
 = V B d
where:
 is the polarization rotation angle,
B is the magnetic field strength,
d is the distance,
V is the "Verdet constant" of the material.

## Slide 17: To model the effect of a medium on light's polarization state, we use Jones matrices.
Since we can write a polarization state as a (Jones) vector, we use
matrices, A, to transform them from the input polarization, E0, to the
output polarization, E1.
This yields:
For example, an x-polarizer can be written:
So:

## Slide 18: Other Jones matrices
A y-polarizer:
A half-wave plate:
A half-wave plate rotates 45-degree-polarization to -45-degree, and vice versa.
A quarter-wave plate:

## Slide 19: A wave plate is not a wave plate if it’s oriented wrong.
Remember that a wave plate wants ±45° (or circular) polarization.
If it sees, say, x polarization, nothing happens.
So use Jones matrices until you’re really on top of this!!!
AHWP
Wave plate w/ axes at 0° or 90°
0° or 90° Polarizer

## Slide 20: Rotated Jones matrices
Okay, so E1 = A E0. What about when the polarizer or wave plate
responsible for A is rotated by some angle, ?
Rotation of a vector by an angle  means multiplication by a rotation
matrix:
where:
Rotating E1 by  and inserting the identity matrix R()-1 R(), we have:
Thus:

## Slide 21: Rotated Jones matrix for a polarizer
Applying this result to an x-polarizer:
for small angles, 

## Slide 22: Jones Matrices for standard components

## Slide 23: To model the effect of many media on light's polarization state, we use many Jones matrices.
To model the effects of more than one component on the polarization state, just multiply the input polarization Jones vector by all of the Jones matrices:
Remember to use the correct order!
A single Jones matrix (the product of the individual Jones matrices) can describe the combination of several components.

## Slide 24: Multiplying Jones Matrices
Crossed polarizers:
x
y
z
x-pol
y-pol
so no light leaks through.
Uncrossed polarizers
(slightly):
rotated
x-pol
y-pol
So Iout ≈2 Iin,x

## Slide 25: Recall that, when the phases of the x- and y-polarizations fluctuate, the light is "unpolarized."
where x(t) and y(t) are functions that vary on a time scale slower than
1/, but faster than you can measure.
The polarization state (Jones vector) will be:
Unfortunately, this is difficult to analyze using Jones matrices.
In practice, the amplitudes vary, too!

## Slide 26: Stokes Parameters
To treat fully, partially, or unpolarized light, we define "Stokes parameters."
Suppose we have four detectors, three with polarizers in front of them:
#0 detects total irradiance............................................I0
#1 detects horizontally polarized irradiance..........…...I1
#2 detects +45° polarized irradiance............................I2
#3 detects right circularly polarized irradiance.....…….I3
The Stokes parameters:
S0  I0 S1  2I1 – I0 S2  2I2 – I0 S3  2I3 – I0
= 1 for polarized light
= 0 for unpolarized light

## Slide 27: Poincaré sphere
We can present the polarization state as a point on the surface of a sphere of radius:
along equator are linearly polarized light at different angles
North and South poles are circular polarization
other points are elliptically polarized
horizontal
vertical
+45
–45
LHC
RHC

## Slide 28: Mueller Matrices multiply Stokes vectors
We can write the four Stokes parameters in vector form:
And we can define matrices that multiply them,
just as Jones matrices multiply Jones vectors.
To model the effects of more than one medium on the polarization
state, just multiply the input polarization Stokes vector by all of the
Mueller matrices:
Sout = M3 M2 M1 Sin

## Slide 29: Stokes vectors (and Jones vectors for comparison)

## Slide 30: Mueller Matrices (and Jones Matrices for comparison)