## Slide 1: Fresnel's Equations for Reflection and Refraction
Incident, transmitted, and reflected beams at interfaces
Reflection and transmission coefficients
The Fresnel Equations
Brewster's Angle
Total internal reflection
Power reflectance and transmittance
Phase shifts in reflection
The mysterious evanescent wave

## Slide 2
Definitions: Planes of Incidence and the Interface and the polarizations
Perpendicular (“S”) polarization sticks out of or into the plane of incidence.
Plane of the interface (here the yz plane) (perpendicular to page)
Plane of incidence (here the xy plane) is the plane that contains the incident and reflected k-vectors.
ni
nt
i
r
t
Ei
Er
Et
Interface
x
y
z
Parallel (“P”) polarization lies parallel to the plane of incidence.
Incident medium
Transmitting medium

## Slide 3
Shorthand notation for the polarizations
Perpendicular (S) polarization sticks up out of the plane of incidence.
Parallel (P) polarization lies parallel to the plane of incidence.

## Slide 4: Fresnel Equations
We would like to compute the fraction of a light wave reflected and
transmitted by a flat interface between two media with different refrac-
tive indices. Fresnel was the first to do this calculation.
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface
x
y
z
Beam geometry
for light with its
electric field per-
pendicular to the
plane of incidence
(i.e., out of the page)
It proceeds by considering the boundary conditions at the interface for the electric and magnetic fields of the light waves.
We’ll do the perpendicular polarization first.
For example,

## Slide 5: Boundary Condition for the Electric Field at an Interface
The Tangential Electric Field is Continuous
In other words:
The total E-field in
the plane of the
interface is continuous.
Here, all E-fields are
in the z-direction,
which is in the plane
of the interface (xz), so:
Ei(x, y = 0, z, t) + Er(x, y = 0, z, t) = Et(x, y = 0, z, t)
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface
x
y
z

## Slide 6: Boundary Condition for the Magnetic Field at an Interface
The Tangential Magnetic Field* is Continuous
In other words:
The total B-field in
the plane of the
interface is continuous.
Here, all B-fields are
in the xy-plane, so we take the x-components:
–Bi(x, y=0, z, t) cos(i) + Br(x, y=0, z, t) cos(r) = –Bt(x, y=0, z, t) cos(t)
*It's really the tangential B/, but we're using 0
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface
x
y
z
i
i

## Slide 7: Reflection and Transmission for Perpendicularly (S) Polarized Light
Canceling the rapidly varying parts of the light wave and keeping only the complex amplitudes:

## Slide 8: Reflection & Transmission Coefficients for Perpendicularly Polarized Light

## Slide 9: Simpler expressions for r┴ and t┴
t
i
wi
wt
ni
nt
Note the magnification at an interface, m:
Also let  be the ratio of the refractive indices, nt / ni.
Dividing numerator and denominator of r and t by ni cos(i:

## Slide 10: Fresnel Equations—Parallel electric field
x
y
z
Note that the reflected magnetic field must point into the screen to achieve . The x means “into the screen.”
Note that Hecht uses a different notation for the reflected field, which is confusing! Ours is better!
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface
Beam geometry
for light with its
electric field
parallel to the
plane of incidence
(i.e., in the page)
This B-field points into the page.

## Slide 11: Reflection & Transmission Coefficients for Parallel (P) Polarized Light
For parallel polarized light, B0i - B0r = B0t
and E0icos(i) + E0rcos(r) = E0tcos(t)
Solving for E0r / E0i yields the reflection coefficient, r||:
Analogously, the transmission coefficient, t|| = E0t / E0i, is
These equations are called the Fresnel Equations for parallel polarized light.

## Slide 12: Simpler expressions for r║ and t║
Again, use the magnification, m, and the refractive-index ratio, .
And again dividing numerator and denominator of r and t by ni cos(i:

## Slide 13: Reflection Coefficients for an Air-to-Glass Interface
nair  1 < nglass  1.5
Note that:
Total reflection at  = 90°
for both polarizations
Zero reflection for parallel polarization at Brewster's angle (56.3° for these values of ni and nt).
(We’ll delay a derivation of a formula for Brewster’s angle until we do dipole emission and polarization.)
Incidence angle, i
Reflection coefficient, r
1.0
.5
0
-.5
-1.0
r||
r
┴
0° 30° 60° 90°
Brewster’s angle
r||=0!

## Slide 14: Reflection Coefficients for a Glass-to-Air Interface
nglass  1.5 > nair  1
Note that:
Total internal reflection
above the critical angle
crit  arcsin(nt /ni)
(The sine in Snell's Law
can't be > 1!):
sin(crit)  nt /ni sin(90)
Incidence angle, i
Reflection coefficient, r
1.0
.5
0
-.5
-1.0
r||
r
┴
0° 30° 60° 90°
Total internal reflection
Brewster’s angle
Critical
angle
Critical
angle

## Slide 15: Transmittance (T)
T  Transmitted Power / Incident Power
t
i
wi
wt
ni
nt
A = Area
Compute the ratio of the beam areas:
The beam expands in one dimension on refraction.
The Transmittance is also called the Transmissivity.
1D beam expansion

## Slide 16: Reflectance (R)
R  Reflected Power / Incident Power
Because the angle of incidence = the angle of reflection, the beam area doesn’t change on reflection.
Also, n is the same for both incident and reflected beams.
So:
A = Area
i
wi
ni
nt
r
wi
The Reflectance is also called the Reflectivity.

## Slide 17: Reflectance and Transmittance for an Air-to-Glass Interface
Note that R + T = 1
Perpendicular polarization
Incidence angle, i
1.0
.5
0
0° 30° 60° 90°
R
T
Parallel polarization
Incidence angle, i
1.0
.5
0
0° 30° 60° 90°
R
T

## Slide 18: Reflectance and Transmittance for a Glass-to-Air Interface
Note that R + T = 1
Perpendicular polarization
Incidence angle, i
1.0
.5
0
0° 30° 60° 90°
R
T
Parallel polarization
Incidence angle, i
1.0
.5
0
0° 30° 60° 90°
R
T

## Slide 19: Reflection at normal incidence
When i = 0,
and
For an air-glass interface (ni = 1 and nt = 1.5),
R = 4% and T = 96%
The values are the same, whichever direction the light travels, from air to glass or from glass to air.
The 4% has big implications for photography lenses.

## Slide 20: Practical Applications of Fresnel’s Equations
Windows look like mirrors at night (when you’re in the brightly lit room)
One-way mirrors (used by police to interrogate bad guys) are just partial reflectors (actually, aluminum-coated).
Disneyland puts ghouls next to you in the haunted house using partial reflectors (also aluminum-coated).
Lasers use Brewster’s angle components to avoid reflective losses:
Optical fibers use total internal reflection. Hollow fibers use high-incidence-angle near-unity reflections.
R = 100%
R = 90%
Laser medium
0% reflection!
0% reflection!

## Slide 21: Phase Shift in Reflection (for Perpendicularly Polarized Light)
So there will be destructive interference between the incident and reflected beams just before the surface.
Analogously, if ni > nt (glass to air), r > 0, and there will be constructive interference.
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface

## Slide 22: Phase Shift in Reflection (Parallel Polarized Light)
This also means destructive interference with incident beam.
Analogously, if ni > nt (glass to air), r|| > 0, and we have constructive interference just above the interface.
Good that we get the same result as for r; it’s the same problem when i = 0! Also, the phase is opposite above Brewster’s angle.
ni
nt
i
r
t
Ei
Bi
Er
Br
Et
Bt
Interface

## Slide 23: Phase shifts in reflection (air to glass)
ni < nt
180° phase shift
for all angles
180° phase shift
for angles below
Brewster's angle;
0° for larger angles
0° 30° 60° 90°
Incidence angle
0° 30° 60° 90°
Incidence angle

0

0
┴
||

## Slide 24: Phase shifts in reflection (glass to air)
nt < ni
Interesting phase above the critical angle
180° phase shift
for angles below
Brewster's angle;
0° for larger angles
0° 30° 60° 90°
Incidence angle
0° 30° 60° 90°
Incidence angle

0

0
┴
||

## Slide 25: Phase shifts vs. incidence angle and ni /nt
Li Li, OPN, vol. 14, #9, pp. 24-30, Sept. 2003
ni /nt
ni /nt
Note the general behavior above and below the various interesting angles…
i
i

## Slide 26: If you slowly turn up a laser intensity incident on a piece of glass, where does damage happen first, the front or the back?
The obvious answer is the front of the object, which sees the higher intensity first.
But constructive interference happens at the back surface between the incident light and the reflected wave.
This yields an irradiance that is 44% higher just inside the back surface!

## Slide 27: Phase shifts with coated optics
Reflections with different magnitudes can be generated using partial metallization or coatings. We’ll see these later.
But the phase shifts on reflection are the same! For near-normal incidence:
180° if low-index-to-high and 0 if high-index-to-low.
Example:
Laser Mirror
Highly reflecting coating on this surface
Phase shift of 180°

## Slide 28: Total Internal Reflection occurs when sin(t) > 1, and no transmitted beam can occur.
Note that the irradiance of the transmitted beam goes to zero (i.e., TIR occurs) as it grazes the surface.
Total internal reflection is 100% efficient, that is, all the light is reflected.
Brewster’s angle
Total Internal Reflection

## Slide 29: Applications of Total Internal Reflection
Beam steerers
Beam steerers
used to compress
the path inside
binoculars

## Slide 30: Fiber Optics
Optical fibers use TIR to transmit light long distances.
They play an ever-increasing role in our lives!
Notes: The purpose of this presentation is to provide a conceptual understanding of how fiber optics are used in communications systems.

## Slide 31: Design of optical fibers
Core: Thin glass center of the fiber that carries the light
Cladding: Surrounds the core and reflects the light back into the core
Buffer coating: Plastic protective coating
ncore > ncladding
Notes: From http://electronics.howstuffworks.com/fiber-optic.htm/printable
The glass is formed by reacting silicon and germanium with oxygen, forming silicon dioxide (SiO2) and germanium dioxide (GeO2). The silicon dioxide and germanium dioxide deposit on the inside of the tube and fuse together to form glass.

## Slide 32: Propagation of light in an optical fiber
Some signal degradation occurs due to imperfectly constructed glass used in the cable. The best optical fibers show very little light loss -- less than 10%/km at 1,550 nm.
Maximum light loss occurs at the points of maximum curvature.
Light travels through the core bouncing from the reflective walls. The walls absorb very little light from the core allowing the light wave to travel large distances.
Notes: From http://electronics.howstuffworks.com/fiber-optic.htm/printable
The light in a fiber-optic cable travels through the core (hallway) by constantly bouncing from the cladding (mirror-lined walls), a principle called total internal reflection. Because the cladding does not absorb any light from the core, the light wave can travel great distances. However, some of the light signal degrades within the fiber, mostly due to impurities in the glass. The extent that the signal degrades depends on the purity of the glass and the wavelength of the transmitted light (for example, 850 nm = 60 to 75 percent/km; 1,300 nm = 50 to 60 percent/km; 1,550 nm is greater than 50 percent/km). Some premium optical fibers show much less signal degradation -- less than 10 percent/km at 1,550 nm.

## Slide 33: Microstructure fiber
Such fiber has many applications, from medical imaging to optical clocks.
Photographs courtesy of Jinendra Ranka, Lucent
Air holes
Core
In microstructure fiber, air holes act as the cladding surrounding a glass core. Such fibers have different dispersion properties.

## Slide 34: Frustrated Total Internal Reflection
By placing another surface in contact with a totally internally
reflecting one, total internal reflection can be frustrated.
How close do the prisms have to be before TIR is frustrated?
This effect provides evidence for evanescent fields—fields that leak through the TIR surface–and is the basis for a variety of spectroscopic techniques.
n
n
n
n
Total internal reflection
Frustrated total internal reflection
n=1
n=1

## Slide 35: FTIR and fingerprinting
See TIR from a fingerprint valley and FTIR from a ridge.
Notes: Picture on right due to Center for Image Processing in Education

## Slide 36: The Evanescent Wave
The evanescent wave is the "transmitted wave" when total internal reflection occurs. A mystical quantity! So we'll do a mystical derivation:
ni
nt
i
t
x
y

## Slide 37: The Evanescent-Wave k-vector
The evanescent wave k-vector must have x and y components:
Along surface: ktx = kt sin(t)
Perpendicular to it: kty = kt cos(t)
Using Snell's Law, sin(t) = (ni /nt) sin(i), so ktx is meaningful.
And again: cos(t) = [1 – sin2(t)]1/2 = [1 – (ni /nt)2 sin2(i)]1/2
= ± i
Neglecting the unphysical -i solution, we have:
Et(x,y,t) = E0 exp[–ky] exp i [ k (ni /nt) sin(i) x – t ]
The evanescent wave decays exponentially in the transverse direction.
ni
nt
i
t
x
y

## Slide 38: Optical Properties of Metals
A simple model of a metal is a gas of free electrons (the Drude model).
These free electrons and their accompanying positive nuclei can
undergo "plasma oscillations" at frequency, p.
where:

## Slide 39: Reflection from metals
At normal incidence in air:
Generalizing to complex refractive indices: