## Slide 1: Geometrical Optics
Geometrical light rays
Ray matrices and ray vectors
Matrices for various optical components
The Lens Maker’s Formula
Imaging and the Lens Law
Mapping angle to position
Cylindrical lenses
Aberrations
The Eye

## Slide 2: Ray Optics
We'll define light rays as directions in space, corresponding, roughly, to k-vectors of light waves.
We won’t worry about the phase.
Each optical system will have an axis, and all light rays will be assumed to propagate at small angles to it. This is called the Paraxial Approximation.
axis

## Slide 3: The Optic Axis
A mirror deflects the optic axis into a new direction.
This ring laser has an optic axis that scans out a rectangle.
Optic axis
A ray propagating through this system
We define all rays relative to the relevant optic axis.

## Slide 4: The Ray Vector
A light ray can be defined by two co-ordinates:
xin, in
xout, out
its position, x
its slope, 
Optical axis
optical ray
x

These parameters define a ray vector, which will change with distance and as the ray propagates through optics.

## Slide 5: Ray Matrices
For many optical components, we can define 2 x 2 ray matrices.
An element’s effect on a ray is found by multiplying its ray vector.
Ray matrices
can describe
simple and com-
plex systems.
These matrices are often called ABCD Matrices.
Optical system ↔ 2 x 2 Ray matrix

## Slide 6: Ray matrices as derivatives
We can write these equations in matrix form.
angular magnification
spatial magnification
Since the displacements and angles are assumed to be small, we can think in terms of partial derivatives.

## Slide 7: For cascaded elements, we simply multiply ray matrices.
Notice that the order looks opposite to what it should be, but it makes sense when you think about it.
O1
O3
O2

## Slide 8: Ray matrix for free space or a medium
If xin and in are the position and slope upon entering, let xout and out be the position and slope after propagating from z = 0 to z.
xin, in
z = 0
xout out
z
Rewriting these expressions in matrix notation:

## Slide 9: Ray Matrix for an Interface
At the interface, clearly:
xout = xin.
Now calculate out.
Snell's Law says: n1 sin(in) = n2 sin(out)
which becomes for small angles: n1 in = n2 out
 out = [n1 / n2] in
in
n1
out
n2
xin
xout

## Slide 10: Ray matrix for a curved interface
At the interface, again:
xout = xin.
To calculate out, we must calculate 1 and 2.
If s is the surface slope at the height xin, then
1 = in+ s and 2 = out+ s
If R is the surface radius of curvature, the surface z coordinate will be:
in
n1
out
n2
xin = xout
1
2
s
R
z
s
z = 0

## Slide 11: Ray matrix for a curved interface (cont’d)
Now the output angle depends on the input position, too.
Snell's Law: n1 1 = n2 2
1 = in+ xin / R and 2 = out+ xin / R
n1
n2
1
2

## Slide 12: A thin lens is just two curved interfaces.
We’ll neglect the glass in between (it’s a really thin lens!), and we’ll take n1 = 1.
n=1
R1
R2
n≠1
n=1
This can be written:
The Lens-Maker’s Formula
where:

## Slide 13: Ray matrix for a lens
The quantity, f, is the focal length of the lens. It’s the single most important parameter of a lens. It can be positive or negative.
In a homework problem, you’ll extend the Lens Maker’s Formula to lenses of greater thickness.
If f > 0, the lens deflects rays toward the axis.
f > 0
If f < 0, the lens deflects rays away from the axis.
f < 0
R1 > 0
R2 < 0
R1 < 0
R2 > 0

## Slide 14: Types of lenses
Lens nomenclature
Which type of lens to use (and how to orient it) depends on the aberrations and application.

## Slide 15: A lens focuses parallel rays to a point one focal length away.
f
f
At the focal plane, all rays converge to the z axis (xout = 0) independent of input position.
Parallel rays at a different angle focus at a different xout.
A lens followed by propagation by one focal length:
Assume all input rays have in = 0
For all rays xout = 0!
Looking from right to left, rays diverging from a point are made parallel.

## Slide 16: Spectrometers
f
f
Entrance slit
Diffraction grating
f
f
Camera
To best distinguish different wave- lengths, a slit confines the beam to the optic axis. A lens collimates the beam, and a diffraction grating disperses the colors. A second lens focuses the beam to a point that depends on its beam input angle (i.e., the wavelength).
 
There are many types of spectrom- eters. But they’re all based on the same principle.

## Slide 17: Ray Matrix for a Curved Mirror
Like a lens, a curved mirror will focus a beam. Its focal length is R/2.
Note that a flat mirror has R = ∞ and hence an identity ray matrix.
Consider a mirror with radius of curvature, R, with its optic axis perpendicular to the mirror:
in
out
xin = xout
1
s
R
z
1

## Slide 18
Laser Cavities
Two flat mirrors, the flat-flat laser cavity, is difficult to align and maintain aligned.
Two concave curved mirrors, the usually stable laser cavity, is generally easy to align and maintain aligned.
Two convex mirrors, the unstable laser cavity, is impossible to align!
Mirror curvatures matter in lasers.

## Slide 19
An unstable cavity (or unstable resonator) can work if you do it properly!
In fact, it produces a large beam, useful for high-power lasers, which must have large beams.
Unstable Resonators
The mirror curvatures determine the beam size, which, for a stable resonator, is small (100 m to 1 mm).
An unstable resonator can have a very large beam. But the gain must be high. And the beam has a hole in it.

## Slide 20: Consecutive lenses
f1
f2
Suppose we have two lenses right next to each other (with no space in between).
So two consecutive lenses act as one whose focal length is computed by the resistive sum.
As a result, we define a measure of inverse lens focal length, the diopter. 1 diopter = 1 m-1

## Slide 21: A system images an object when B = 0.
When B = 0, all rays from a point xin arrive at a point xout, independent of angle.
xout = A xin
When B = 0, A is the magnification.

## Slide 22: The Lens Law
From the object to
the image, we have:
1) A distance do
2) A lens of focal length f
3) A distance di
This is the Lens Law.

## Slide 23: Imaging Magnification
If the imaging condition,
is satisfied, then:
So:

## Slide 24: Magnification Power
Often, positive lenses are rated with a single magnification, such as 4x.
In principle, any positive lens can be used at an infinite number of possible magnifications. However, when a viewer adjusts the object distance so that the image appears to be essentially at infinity (which is a comfortable viewing distance for most individuals), the magnification is given by the relationship:
Magnification = 250 mm / f
Thus, a 25-mm focal-length positive lens would be a 10x magnifier.
Object under observation
Notes: Text from Melles Griot
Magnification Power Often, positive lenses intended for use as simple magnifiers are rated with a single magnification, such as 4x. To create a virtual image for viewing with the human eye, in principle, any positive lens can be used at an infinite number of possible magnifications. However, there is usually a narrow range of magnifications that will be comfortable for the viewer. Typically, when the viewer adjusts the object distance so that the image appears to be essentially at infinity (which is a comfortable viewing distance for most individuals), magnification is given by the relationship magnification = 250 mm/f (f in mm). Thus, a 25-mm focal length positive lens would be a 10x magnifier.

## Slide 25
Virtual Images
When the object is less than one focal length away from a lens, no image occurs, but a virtual image is said to occur if you look back through the lens.
Object
f > 0
Virtual image

## Slide 26
f
It depends on how much of the lens is used, that is, the aperture.
Only one plane is imaged (i.e., is in focus) at a time. But we’d like objects near this plane to at least be almost in focus. The range of distances in acceptable focus is called the depth of field.
Out-of-focus plane
Focal plane
Object
Image
Size of blur in out-of-focus plane
Aperture
The smaller the aperture, the more the depth of field.
Depth of Field

## Slide 27: Depth of field example
f/32 (very small aperture; large depth of field)
f/5 (relatively large aperture; small depth of field)
A large depth of field isn’t always desirable.
A small depth of field is also desirable for portraits.
Notes: wikipedia.org

## Slide 28: Bokeh
Poor Bokeh. Edge is sharply defined.
Good Bokeh. Edge is completely undefined.
Neutral Bokeh. Evenly illuminated blur circle. Still bad because the edge is still well defined.
Bokeh is the rendition of out-of-focus points of light.
Something deliberately out of focus should distract.
Bokeh is where art and engineering diverge, since better bokeh is due to an imperfection (spherical aberration). Perfect bokeh is a Gaussian blur, but lenses are usually designed for neutral bokeh!
Notes: http://www.kenrockwell.com/tech/bokeh.htm
Bokeh is different from sharpness. Sharpness is what happens at the point of best focus. Bokeh is what happens away from the point of best focus.
Bokeh describes the appearance or "feel" of out-of-focus backgrounds and foregrounds.
Differing amounts of spherical aberration alter how lenses render out-of-focus points of light, and thus their bokeh. The word "bokeh" comes from the Japanese word "boke" (pronounced bo-keh) which literally means fuzziness or dizziness.
A technically perfect lens has no spherical aberration. Therefore a perfect lens focuses all points of light as cones of light behind the lens. The image is in focus if the film is exactly where the cone reaches its finest point. The better the lens, the tinier this point gets.
If the film is not exactly where that cone of light reaches its smallest point, then that point of the image is not in focus. Then that point is rendered on film as a disk of light, instead instead of as a point. This disc is also called the "blur circle," or "circle of confusion" by people calculating depth-of-field charts. In a lens with no spherical aberration this blur circle is an evenly illuminated disc. Out of focus points all look like perfect discs with sharp edges. (OK, at smaller apertures where the image is in pretty good focus you may see additional "Airy" rings around the circle, but that's a diffraction pattern we're not discussing here.) This isn't optimal for bokeh, since as you can imagine the sharp edge of these discs can start to give definition to things intended to be out-of-focus.
There are no perfect lenses, so one usually does not see these perfect discs.
Real lenses have some degree of spherical aberration. This means that in practice, even though all the light coming through the lens from a point on the subject may meet at a nice, tiny point on the film, that the light distribution within the cone itself may be uneven. Yes, we are getting abstract here, which is why some denser photographers refuse to try understand bokeh.
Illustrations
Spherical aberration means that the discs made by out-of-focus points on the subject will not be evenly illuminated. Instead they tend to have more of the light collect in the middle of the disc or towards the edges. Here are some illustrations:

## Slide 29: The pinhole camera
You can make an entire room into a camera this way by cutting a small hole in a wall and looking at the opposite wall. This is called the camera obscura.
Object
Image
Pinhole
If all light rays are directed through a pinhole, it forms an image with an infinite depth of field.
The first person to mention this idea was Aristotle.
The concept of the focal length is inappropriate for a pinhole lens. The magnification is still –di/do.
Notes: The term camera obscura was probably coined by Giambattista della Porta (1535-1615) (or maybe he read it in a previous work), and it means “dark room” in Latin. Renaissance painters almost certainly used them to paint realistic paintings. Vermeer painted “The Girl with a Pearl Earring” (1665-7) using one. Facts taken from Jaroszewicz, et al., OPN April 2005.
A nice view of a camera obscura is in the movie, “Addicted to Love,” starring Matthew Broderick (who plays an astronomer) and Meg Ryan, who set one up to spy on their former lovers.

## Slide 30
The F-number, “f / #”, of a lens is the ratio of its focal length and its diameter.
f / # = f / d
f
f
d1
f
f
d2
f / # = 1
f / # = 2
Large f-number lenses collect more light but are harder to engineer.
F-number

## Slide 31
Another measure of a lens size is the numerical aperture. It’s the product of the medium refractive index and the marginal ray angle.
NA = n sin()
High-numerical-aperture lenses are bigger.
f

Numerical Aperture
Why this definition? Because the magnification can be shown to be the ratio of the NA on the two sides of the lens.
Notes: Numerical Aperture and Magnification The magnification of the system is equal to the ratio of the numerical apertures on the object and image sides of the system. This powerful and useful result is completely independent of the specifics of the optical system, and it can often be used to determine the optimum lens diameter in situations involving aperture constraints. When a lens or optical system is used to create an image of a source, it is natural to assume that, by increasing the diameter (f) of the lens, we will be able to collect more light and thereby produce a brighter image. However, because of the relationship between magnification and numerical aperture, there can be a theoretical limit beyond which increasing the diameter has no effect on light-collection efficiency or image brightness. Since the numerical aperture of a ray is given by f/2s, once a focal length and magnification have been selected, the value of NA sets the value of f. Thus, if one is dealing with a system in which the numerical aperture is constrained on either the object or image side, increasing the lens diameter beyond this value will increase system size and cost but will not improve performance (i.e., throughput or image brightness). This concept is sometimes referred to as the optical invariant.

## Slide 32: Lenses can also map angle to position.
So
And this arrangement
maps position to angle:
From the object to
the image, we have:
1) A distance f
2) A lens of focal length f
3) A distance f

## Slide 33: Telescopes
A telescope should image an object, but, because the object will have a very small solid angle, it should also increase its solid angle significantly, so it looks bigger. So we’d like D to be large. And use two lenses to square the effect.
where M = - di / do
So use di << do for both lenses.
Note that this is easy for the first lens, as the object is really far away!
M1
M2
Image plane #1
Image plane #2
Keplerian telescope

## Slide 34
Telescope Terminology

## Slide 35: Telescopes (cont’d)
The Galilean Telescope
f1 < 0
f2 > 0
The analysis of this telescope is a homework problem!

## Slide 36: The Cassegrain Telescope
Telescopes must collect as much light as possible from the generally very dim objects many light-years away.
It’s easier to create large mirrors than large lenses (only the surface needs to be very precise).
Object
It may seem like the image will have a hole in it, but only if it’s out of focus.

## Slide 37: The Cassegrain Telescope
If a 45º-mirror reflects the beam to the side before the smaller mirror, it’s called a Newtonian telescope.
Notes: Designers of telescopes faced the problem of chromatic aberrations—that is, until Isaac Newton solved it. In 1672, Newton published a seminal paper on light and color, in which he showed that white light is a mixture of all colors of the spectrum. When white light passes through a curved lens it breaks down into its various component colors, each of which comes into focus at a different point on the optical axis—hence the color fringes seen in refractors.
Other scientists had speculated that using mirrors rather than lenses might correct this problem, but Newton was the first to put such thoughts into practice. He cast a two-inch metal mirror and ground it so that it had a spherical curvature. He placed the mirror at one end of a tube. Light coming in the other end reflected off the mirror back toward the opening. The reflected light struck a secondary mirror Newton had affixed inside the tube at a 45-degree angle. That secondary mirror, in turn, bounced the light (and thus the image seen) into a convex eyepiece lens built into the side of the tube.
This was the first working reflecting telescope. Other designers proved unable to grind mirrors with a regular curvature, so the reflector remained largely a curiosity until the mid-18th century, when it finally began to come into its own.
Animation and above text due to http://www.pbs.org/wgbh/nova/galileo/telescope.html

## Slide 38: No discussion of telescopes would be complete without a few pretty pictures.
NGC 6543-Cat's Eye Nebula-one of the most complex planetary nebulae ever seen
Galaxy Messier 81
Uranus is surrounded by its four major rings and by 10 of its 17 known satellites
Notes: Pictures from Optics I student project, Yujiro Ito, 2004.
Images from http://hubblesite.org/ and http://www.spitzer.caltech.edu/

## Slide 39
Micro-scopes
M1
M2
Image plane #1
Image plane #2
Microscopes work on the same principle as telescopes, except that the object is really close and we wish to magnify it.
When two lenses are used, it’s called a compound microscope.
Standard distances are s = 250 mm for the eyepiece and s = 160 mm for the objective, where s is the image distance beyond one focal length. In terms of s, the magnification of each lens is given by:
|M| = di / do = (f + s) [1/f – 1/(f+s)] = (f + s) / f – 1 = s / f
Eye- piece
Many creative designs exist for microscope objectives. Example: the Burch reflecting microscope objective:
Objective
Object
To eyepiece

## Slide 40: If an optical system lacks cylindrical symmetry, we must analyze its x- and y-directions separately: Cylindrical lenses
A "spherical lens" focuses in both transverse directions.
A "cylindrical lens" focuses in only one transverse direction.
When using cylindrical lenses, we must perform two separate ray-matrix analyses, one for each transverse direction.

## Slide 41: Large-angle reflection off a curved mirror also destroys cylindrical symmetry.
Optic axis before reflection
Optic axis after reflection
The optic axis makes a large angle with the mirror normal, and rays make an angle with respect to it.
Rays that deviate from the optic axis in the plane of incidence are called "tangential.”
Rays that deviate from the optic axis  to the plane of incidence are called "sagittal.“ (We need a 3D display to show one of these.)
tangential ray

## Slide 42: Ray Matrix for Off-Axis Reflection from a Curved Mirror
If the beam is incident at a large angle, , on a mirror with radius of curvature, R:
where Re = R cos for tangential rays
and Re = R / cos for sagittal rays
R
Optic axis
tangential ray


## Slide 43: Aberrations
Aberrations are distortions that occur in images, usually due to imperfections in lenses, some unavoidable, some avoidable.
They include:
Chromatic aberration
Spherical aberration
Astigmatism
Coma
Curvature of field
Pincushion and Barrel distortion
Most aberrations can’t be modeled with ray matrices. Designers beat them with lenses of multiple elements, that is, several lenses in a row. Some zoom lenses can have as many as a dozen or more elements.
Notes: Image and text taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 44: Chromatic Aberration
Because the lens material has a different refractive index for each wavelength, the lens will have a different focal length for each wavelength. Recall the lens-maker’s formula:
Here, the refractive index is larger for blue than red, so the focal length is less for blue than red.
You can model spherical aberration using ray matrices, but only one color at a time.

## Slide 45: Chromatic aberration can be minimized using additional lenses
In an Achromat, the second lens cancels the dispersion of the first.
Achromats use two different materials, and one has a negative focal length.
Notes: Image from Melles Griot catalog.

## Slide 46: Spherical Aberration in Mirrors
For all rays to converge to a point a distance f away from a curved mirror requires a paraboloidal surface.
But this only works for rays with in = 0.
Spherical surface
Paraboloidal surface

## Slide 47: Spherical Aberration in Lenses
So we use spherical surfaces, which work better for a wider range of input angles.
Nevertheless, off-axis rays see a different focal length, so lenses have spherical aberration, too.

## Slide 48: Minimizing spherical aberration in a focus
Plano-convex lenses (with their flat surface facing the focus) are best for minimizing spherical aberration when focusing.
One-to-one imaging works best with a symmetrical lens (q = ∞).
R1 = Front surface radius of curvature
R2 = Back surface radius of curvature
Notes: Plot and text below from Melles Griot
Aberrations are highly dependent on application, lens shape, and material of the lens (or, more exactly, its index of refraction). The singlet shape that minimizes spherical aberration at a given conjugate ratio is called best-form. The criterion for best-form at any conjugate ratio is that the marginal rays are equally refracted at each of the lens/air interfaces. This minimizes the effect of sinq not equal to q. It is also the criterion for minimum surface-reflectance loss. Another benefit is that absolute coma is nearly minimized for best-form shape, at both infinite and unit conjugate ratios. To further explore the dependence of aberrations on lens shape, it is helpful to make use of the Coddington shape factor, q, defined as The figure shows the transverse and longitudinal spherical aberration of a singlet lens as a function of the shape factor, q. In this particular instance, the lens has a focal length of 100 mm, operates at f/# = 5, has an index of refraction of 1.518722 (BK7 at the mercury green line, 546.1 nm), and is being operated at the infinite conjugate ratio. It is also assumed that the lens itself is the aperture stop. An asymmetric shape that corresponds to a q-value of about 0.7426 for this material and wavelength is the best singlet shape for on-axis imaging. Best-form shapes are used in Melles Griot laser-line-focusing singlet lenses. It is important to note that the best-form shape is dependent on refractive index. For example, with a high-index material, such as silicon, the best-form lens for the infinite conjugate ratio is a meniscus shape.
At infinite conjugate with a typical glass singlet, the plano-convex shape (q = 1), with convex side toward the infinite conjugate, performs nearly as well as the best-form lens. Because a plano-convex lens costs much less to manufacture than an asymmetric biconvex singlet, these lenses are quite popular. Furthermore, this lens shape exhibits near-minimum total transverse aberration and near-zero coma when used off axis, thus enhancing its utility. For imaging at unit magnification (s = s" = 2f ), a similar analysis would show that a symmetric biconvex lens is the best shape. Not only is spherical aberration minimized, but coma, distortion, and lateral chromatic aberration exactly cancel each other out. These results are true regardless of material index or wavelength, which explains the utility of symmetric convex lenses, as well as symmetrical optical systems in general. However, if a remote stop is present, these aberrations may not cancel each other quite as well. For wide-field applications, the best-form shape is definitely not the optimum singlet shape, especially at the infinite conjugate ratio, since it yields maximum field curvature. The ideal shape is determined by the situation and may require rigorous ray-tracing analysis. It is possible to achieve much better correction in an optical system by using more than one element. The cases of an infinite conjugate ratio system and a unit conjugate ratio system are discussed in the following section.

## Slide 49: Spherical aberration can be also minimized using additional lenses
The additional lenses cancel the spherical aberration of the first.
Notes: Image from Melles Griot catalog.

## Slide 50: Astigmatism
When the optical system lacks perfect cylindrical symmetry, we say it has astigmatism. A simple cylindrical lens or off-axis curved-mirror reflection will cause this problem.

Cure astigmatism with another cylindrical lens or off-axis curved mirror.
Model astigmatism by separate x and y analyses.
Notes: Image and text taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 51: Coma
Coma causes rays from an off-axis point of light in the object plane to create a trailing "comet-like" blur directed away from the optic axis. A lens with considerable coma may produce a sharp image in the center of the field, but become increasingly blurred toward the edges. For a single lens, coma can be caused or partially corrected by tilting the lens.
Notes: Image and text taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 52: Curvature of field
Curvature of field causes a planar object to project a curved (non-planar) image. Rays at a large angle see the lens as having an effectively smaller diameter and an effectively smaller focal length, forming the image of the off axis points closer to the lens.
Notes: Image and text taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 53: Pincushion and Barrel Distortion
These distortions are fixed by an “orthoscopic doublet” or a “Zeiss orthometer.”
Notes: Other than distortions from lens imperfections, certain distortions occur from the geometry of the lens. The barrel and pincushion distortions below can be readily seen in the image formed by a thick double convex glass lens. They are the reason for a practical limitation in the magnification achievable from a simple magnifier. These distortions are minimized by using symmetric doublets such as the orthoscopic doublet and eyepieces such as the Ramsden eyepiece. Image and text taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 54: Barrel and pincushion distortion
Barrel
Pincushion
Notes: Wikipedia.com

## Slide 55: Photography lenses
Double Gauss
Petzval
Photography lenses are complex! Especially zoom lenses.
These are older designs.
Notes: Images taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 56: Photography lenses
Modern lenses can have up to 20 elements!
Canon EF 600mm f/4L IS USM Super Telephoto Lens
17 elements in 13 groups
$12,000
Canon 17-85mm f/3.5-4.5 zoom
Notes: Images taken from http://hyperphysics.phy-astr.gsu.edu

## Slide 57: Geometrical Optics terms
Notes: Image borrowed from Melles Griot

## Slide 58: Anatomy of the Eye
Eye slides courtesy of Prasad Krishna, Optics I student 2003.
Incoming light
Notes: Reference: HowStuffWorks.com

## Slide 59: The cornea, iris, and lens
The cornea is a thin membrane that has an index of refraction of around 1.38. It protects the eye and refracts light (more than the lens does!) as it enters the eye. Some light leaks through the cornea, especially when it’s blue.
The iris controls the size of the pupil, an opening that allows light to enter through.
The lens is jelly-like lens with an index of refraction of about 1.44. This lens bends so that the vision process can be fine tuned.
When you squint, you are bending this lens and changing its properties so that your vision is clearer.
The ciliary muscles bend and adjust the lens.

## Slide 60: Near-sightedness (myopia)
In nearsightedness, a person can see nearby objects well, but has difficulty seeing distant objects. Objects focus before the retina. This is usually caused by an eye that is too long or a lens system that has too much power to focus.
Myopia is corrected with a negative-focal-length lens. This lens causes the light to diverge slightly before it enters the eye.
Near-sightedness

## Slide 61: Far-sightedness (hyperopia)
Far-sightedness (hyperopia) occurs when the focal point is beyond the retina. Such a person can see distant objects well, but has difficulty seeing nearby objects. This is caused by an eye that is too short, or a lens system that has too little focusing power. Hyperopia is corrected with a positive-focal-length lens. The lens slightly converges the light before it enters the eye.
Far-sightedness
As we age, our lens hardens, so we’re less able to adjust and more likely to experience far-sightedness. Hence “bifocals.”

## Slide 62: Astigmatism is a common problem in the eye.
Notes: Image from http://hyperphysics.phy-astr.gsu.edu/hbase/vision/eyedef.html#c5

## Slide 63: Is geometrical optics the whole story?
No. We neglected the phase.
Also, our ray pictures seem to imply that, if we could just remove all aberrations, we could focus a beam to a point and obtain infinitely good spatial resolution.
Not true. The smallest possible focal spot is the wavelength, . Same for the best spatial resolution of an image. This is due to diffraction, which has not been included in geometrical optics.
>
~0