## Slide 1: Diffraction and the Fourier Transform
Light bends!
Diffraction assumptions
Solution to Maxwell's
Equations
The near field
Fresnel Diffraction
Some examples
The far-field
Fraunhofer Diffraction
Some examples

## Slide 2: Diffraction
Light does not always travel in a straight line.
It tends to bend around objects. This tendency is called diffraction.
Any wave will do this, including matter waves and acoustic waves.
Shadow of a hand
illuminated by a
Helium-Neon laser
Shadow of a zinc oxide
crystal illuminated by a
electrons

## Slide 3: Why it’s hard to see diffraction
Diffraction tends to cause ripples at edges. But poor source temporal or spatial coherence masks them.
Example: a large spatially incoherent source (like the sun) casts blurry shadows, masking the diffraction ripples.
Untilted rays yield a perfect shadow of the hole, but off-axis rays blur the shadow.
Screen
with hole
A point source is required.

## Slide 4: Diffraction of a wave by a slit
Whether waves in water or electromagnetic radiation in air, passage through a slit yields a diffraction pattern that will appear more dramatic as the size of the slit approaches the wavelength of the wave.

## Slide 5: Diffraction of ocean water waves
Ocean waves passing through slits in Tel Aviv, Israel
Diffraction occurs for all waves, whatever the phenomenon.

## Slide 6: Diffraction by an Edge
Light passing by edge
Electrons passing by an edge (Mg0 crystal)
x
Transmission
Even without a small slit, diffraction can be strong.
Simple propagation past an edge yields an unintuitive irradiance pattern.

## Slide 7: Radio waves diffract around mountains.
When the wavelength is km long, a mountain peak is a very sharp edge!
Another effect that occurs is scattering, so diffraction’s role is not obvious.

## Slide 8: Diffraction Geometry
We wish to find the light electric field after a screen with a hole in it.
This is a very general problem with far-reaching applications.
What is E(x1,y1) at a distance z from the plane of the aperture?
Incident wave
This region is assumed to be much smaller than this one.
x1
x0
P1
0
A(x0,y0)
y1
y0

## Slide 9: Diffraction Assumptions
The best assumptions were determined by Kirchhoff:
1) Maxwell's equations
2) Inside the aperture, the field and its spatial derivative are the same as if the screen were not present.
3) Outside the aperture (in the shadow of the screen), the field and its spatial derivative are zero.
While these assumptions give the best results, they actually over-determine the problem and can be shown to yield zero field everywhere! Nevertheless, we still use them.
Incident wave

## Slide 10: Diffraction Solution
The field in the observation plane, E(x1,y1), at a distance z from the aperture plane is given by a convolution:
A very complicated result! And we cannot approximate r01 in the exp by z because it gets multiplied by k, which is big, so relatively small changes in r01 can make a big difference!

## Slide 11: Fresnel Diffraction: Approximations
But, in the denominator, we can approximate r01 by z.
And, in the numerator, we can write:
This yields:

## Slide 12: Fresnel Diffraction: Approximations
Multiplying out the squares:
This is the Fresnel integral. It's complicated!
It yields the light wave field at the distance z from the screen.
Factoring out the quantities independent of x0 and y0:

## Slide 13: Diffraction Conventions
We’ll typically assume that a plane wave is incident on the aperture.
And we’ll explicitly write the aperture function in the integral:
And we’ll usually ignore the various factors in front:
It still has an exp[i(t – k z)], but it’s constant with respect to x0 and y0.

## Slide 14: Fresnel Diffraction: Example
Fresnel Diffraction from a single slit:
Far from the slit
z
Close to the slit
Incident plane wave
Slit

## Slide 15: Fresnel Diffraction from a Slit
This irradiance vs. position emerges from a slit illuminated by a laser.
x1
Irradiance

## Slide 16: The Spot of Arago
If a beam encounters a stop, it develops a hole, which fills in as it propagates and diffracts:
This irradiance can be quite high and can do some damage!
Interestingly, the hole fills in from the center first!
x0
x1
Stop
Beam after some distance
Input beam with hole
Notes: Also called Poisson’s spot. It was Poisson (who adhered to the particle-theory of light) who pointed out the “contradiction” of this spot and concluded that it showed why the wave theory of light should be abandoned. Arago then did the experiment, which confirmed the existence of the spot. But G.F. Maraldi actually observed the spot almost a century earlier.

## Slide 17: Diffraction Approximated
The approximate intensity vs. position from an edge:
Such effects can be modeled by measuring the distance on a “Cornu Spiral”
But most useful diffraction effects do not occur in the Fresnel diffraction regime because it’s too complex.
For a cool Java applet that computes Fresnel diffraction patterns, try http://falstad.com/diffraction/

## Slide 18: Fraunhofer Diffraction: The Far Field
Let D be the size of the aperture: D 2 = x02 + y02.
When kD2/2z << 1, the quadratic terms << 1, so we can neglect them:
Recall the Fresnel diffraction result:
This condition corresponds to going far away: z >> kD2/2 = D2/
If D = 100 microns and  = 1 micron, then z >> 30 meters, which is far!

## Slide 19: Fraunhofer Diffraction Conventions
As in Fresnel diffraction, we’ll neglect the phase factors, and we’ll explicitly write the aperture function in the integral:
This is just a Fourier Transform!
Interestingly, it’s a Fourier Transform from position, x0, to another position variable, x1 (in another plane). Usually, the Fourier “conjugate variables” have reciprocal units (e.g., t & , or x & k). The conjugate variables here are really x0 and kx = kx1/z, which have reciprocal units.
So the far-field light field is the Fourier Transform of the apertured field!
E(x0,y0) = constant if a plane wave

## Slide 20: The Fraunhofer Diffraction formula
where we’ve dropped the subscripts, 0 and 1,
E(x,y) = const if a plane wave
Aperture function
We can write this result in terms of the off-axis k-vector components:
kx = kx1/z and ky = ky1/z
kz
ky
kx
x = kx /k = x1/z and y = ky /k = y1/z
and:
or:

## Slide 21: Fraunhofer Diffraction from a slit
Fraunhofer Diffraction from a slit is simply the Fourier Transform of a rect function, which is a sinc function. The irradiance is then sinc2 .

## Slide 22: Fraunhofer Diffraction from a Square Aperture
The diffracted field is a sinc function in both x1 and y1 because the Fourier transform of a rect function is sinc.
Diffracted
irradiance
Diffracted
field

## Slide 23: Diffraction from a Circular Aperture
A circular aperture
yields a diffracted
"Airy Pattern,"
which involves a
Bessel function.
Diffracted field
Diffracted Irradiance

## Slide 24: Diffraction from small and large circular apertures
Recall the Scale Theorem!
Far-field intensity pattern from a small aperture
Far-field intensity pattern from a large aperture

## Slide 25: Fraunhofer diffraction from two slits
A(x0) = rect[(x0+a)/w] + rect[(x0-a)/w]
0
x0
a
-a
kx1/z
w
w

## Slide 26: Diffraction from one- and two-slit screens
Fraunhofer diffraction patterns
One slit
Two slits

## Slide 27: Diffraction from multiple slits
Slit Diffraction
Pattern Pattern
Infinitely many equally spaced slits (a Shah function!) yields a far-field pattern that’s the Fourier transform, that is, the Shah function.

## Slide 28: Young’s Two Slit Experiment and Spatial Coherence
If the spatial coherence length is less than the slit separation, then the relative phase of the light transmitted through each slit will vary randomly, washing out the fine-scale fringes, and a one-slit pattern will be observed.
Fraunhofer diffraction patterns
Good spatial coherence
Poor spatial coherence

## Slide 29: Young’s Two Slit Experiment and Quantum Mechanics
Imagine using a beam so weak that only one photon passes through the screen at a time. In this case, the photon would seem to pass through only one slit at a time, yielding a one-slit pattern.
Which pattern occurs?
Possible Fraunhofer diffraction patterns
Each photon passes through only one slit
Each photon passes through both slits